## Slide 1: DATA FLOW DESCRIPTION

## Slide 2: Packets’ frames
Frame name | Code | Description
ControlLawParameters | CLP | Parameters used in the control law.
CalculatorRecommandations | CR | Recommandations given by a calculator about every calculators (integer value : 1 = trust / 0 = neutral / -1 = don’t trust)
CalculatorFeelings | CF | Trust values given by a calculator about every calculators (real value from 0 to 100).
CalculatorOrders | CO | Control laws given by a calculator that should be applied to actuators (real value : any)
CalculatorOrderValidations | COV | Validation of previous control laws given by all calculators (integer value : 0 = invalid or absent / 1 = valid)
RefereeOrders | RO | Control law to be applied by actuators + orders (activation/desactivation, reinitialisation, reconfiguration, etc.) (real value : any, + enumeration order)

## Slide 3: Sensor data flow
SENSOR
Physical value
RO
CLP
Frame name | Code | Sent from | Received from
ControlLawParameters | CLP | Sensors | Calculator
CalculatorRecommandations | CR | Calculator | Calculator
CalculatorFeelings | CF | Calculator | Referee
CalculatorOrders | CO | Calculator | Calculator & Referee
CalculatorOrderValidations | COV | Calculator | Referee
RefereeOrders | RO | Referee | Calculator & Actuator

## Slide 4: Calculator data flow
CALCULATOR
CO
Frame name | Code | Sent from | Received from
ControlLawParameters | CLP | Sensors | Calculator
CalculatorRecommandations | CR | Calculator | Calculator
CalculatorFeelings | CF | Calculator | Referee
CalculatorOrders | CO | Calculator | Calculator & Referee
CalculatorOrderValidations | COV | Calculator | Referee
RefereeOrders | RO | Referee | Calculator & Actuator
CO
CLP
CR
CF
CR
COV
RO

## Slide 5: Referee data flow
REFEREE
COV
Frame name | Code | Sent from | Received from
ControlLawParameters | CLP | Sensors | Calculator
CalculatorRecommandations | CR | Calculator | Calculator
CalculatorFeelings | CF | Calculator | Referee
CalculatorOrders | CO | Calculator | Calculator & Referee
CalculatorOrderValidations | COV | Calculator | Referee
RefereeOrders | RO | Referee | Calculator & Actuator
CF
CO
RO

## Slide 6: Actuator data flow
ACTUATOR
Frame name | Code | Sent from | Received from
ControlLawParameters | CLP | Sensors | Calculator
CalculatorRecommandations | CR | Calculator | Calculator
CalculatorFeelings | CF | Calculator | Referee
CalculatorOrders | CO | Calculator | Calculator & Referee
CalculatorOrderValidations | COV | Calculator | Referee
RefereeOrders | RO | Referee | Calculator & Actuator
RO